  Visual Servoing Project Report

    Yağmur Çiğdem Aktaş

       November 29, 2021

Contents

1. Abstract	. . . . . . . . . . . . . . . . . . . . 3

2. Introduction & Tools	. . . . . . . . . . . . . . . . . . . . 4

3. Tasks and Their Implementation . . . . . . . . . . . . . . . . . . . . 5

 3.1 Calibration of the Camera

3.2 Real Time Image Handling & Robot’s Current Pose Estimation

3.3 Map Creation, Shortest Path Finding with A* Algorithm & Pose Estimation of each Way	Point

3.4 Calculating Robot Pose in Way Point Coordinate Frame & Navigation of the Robot

3.6 Parking

4. Resources & Conclusion . . . . . . . . . . . . . . . . . . . . 12

Abstract

Path finding and navigation is a frequently encountered task in the field of robotics. Although there are many different methods of transporting a mobile robot from its starting position to a specific destination, in this project, we tried to fulfill this task by using a hand to eye visual servoing system.

Introduction

We carried out a project that processes the pictures taken in real time with a fish eye camera at the top of the environment, calculated the positions of the robot and the target point according to the camera coordinate system, and enabled the robot to reach its target position from this starting position via the shortest path possible. Additional steps such as obstacle avoidance and parking after reaching the target are also among the contents of the project. This project was first prepared on a simulation system and then tested in real time.

Tools

The hardware and the software tools used for this project:

- Turtlebot3 Burger
- FE185C057HA-1 Fish eye Camera
- Ubuntu 20.4
- ROS Noetic

Tasks and Their Implementation

We tried to implement this project, which is full of different tasks and challenges, by dividing it into simple and small steps. The flow chart below shows the general steps and operation of the project. Therefore, we regularly receive information from our fish-eye camera, which overlooks the environment, and use this information to calculate the starting position of the robot and the target, only once at the beginning. By transforming this calculation into a maze map on which we can use the A* algorithm, we calculate the shortest path between the robot's starting position and the target point, taking into account the obstacles. The way points we obtain as a result of the A* algorithm become intermediate target points that the robot must reach one by one during the stage of reaching the target point. In order to ensure correct speed control of the robot in the linear x and angular z directions, the poses of the way points are calculated according to the camera coordinate system. In another words, we go from image plane (pixel coordinates of the way points) to the real world frame.
After this calculation, the following cycle continues until the robot reaches the target point: Calculating the current position of the robot first in the camera coordinate system and then in the coordinate system of the way point to be reached. Calculation of linear x and angular z speeds using PID controller. When the distance between the current position of the robot and the way point position is less than 0.05 m, the required pose calculations for the next way point are made by sending the information that the relevant way point has been reached. When the robot reaches the
target point, parking as the last task is performed by orienting the robot with the same direction of the target pose.

Calibration of the Camera

To be able to use the images coming from the camera, we need to undistort them. For this	purpose we calibrated the camera using a checkerboard and obtained the camera intrinsic,	extrinsic parameters with distortion coefficients.

We used ROS camera_calibration package for this step with following command:
rosrun camera_calibration cameracalibrator.py --size 8x6 --square 0.08	image:=/camera/image_raw camera:=/camera

The main link we used is	http://wiki.ros.org/camera_calibration/Tutorials/MonocularCalibration

Finally, we obtained the following “ost_real.yaml” file obtaining camera parameters.

- Real Time Image Handling

Using the fish eye camera on the top of the environment, we obtain the first image to extract	initial robot position and target position using the Aruco Markers having 15x15 cm size. For	this purpose we have a subscriber which listens to the camera/image_raw topic. In the	callback function of this subscriber, we detect the 4 corner of the markers as the pixel	coordinates in	the image. This first image and initial pixel positions are used for map	creation in the next step.

Apart from the first picture sent for mapping and the initial robot - target detection, this step	is responsible for publishing the current robot position to the estimated_pose topic through a	publisher, by first detecting the current position of the robot on the picture and then	calculating its position according to the camera coordinate system. This step is performed	repeatedly until the whole task is completed.

This task is implemented in real_time_image_subscriber.py file. Main parts and their	explanations of this file is as follows:

sub = rospy.Subscriber('/camera/image_raw', Image, callback) → sub is the main subscriber	to the camera/image_raw topic where our fish eye camera publishes the images

callback(msg) function → callback function of the sub subscriber. In this function, the image	is converted to a numpy array, undistorted with cv2.undistort() function using calibration	parameters. After undistorting, the markers are detected using cv2.aruco.detectMarkers()	function which gives us the id and 4 corners of a detected marker. Using	cv2.aruco.estimatePoseSingleMarkers() function, these 4 corners are used to calculate the	camera frame positions of the markers. This step is the main point to keep tracking the	robot’s current position.

pub = rospy.Publisher('/estimated_pose', MarkerPose, queue_size=1) → pub is the main	publisher variable to send the current pose of the robot to the estimated_pose topic using	MarkerPose user defined message type. This message contains rotational and translational	vectors of the pose.

Map Creation, Shortest Path Finding with A* Algorithm & Pose Estimation of each Way Point

The first image obtained by the camera is saved as “env.png” in	real_time_image_subscriber.py file.

1. At first, robot’s and target’s marker are detected. Since the robot’s marker has the ID 0 and target’s marker has the ID 1, we can easily distinguish which is the robot’s marker detection and which is the target’s marker detection.
2. Secondly, we detect red boxes applying an RGB low – high value mask to our image. After applying this mask, we obtain an image where only the obstacles, robot’s and target’s center points are visible while other pixels are all black.

1. Next step is to create a grid map using these obstacle – non obstacle pixel information.
  A grid map of this image is created using 40x40 pixels of grid boxes. To	obtain a binary image named maze having 0 for free spaces and 1 for obstacles, we travel through our initial image with a 40x40 window size, we put 1 if any obstacle pixel is found	in this window area and 0 otherwise.
2. After obtaining the maze, we can directly apply A* star algorithm giving this maze, robot’s position as start point and target’s position as end point. To convert robot and target pixel positions to the maze pixels, we divide these pixel coordinates by 40 again.
3. A* algorithm gives us the way points and the last step of this part is to convert these way points to the camera frame positions which is done by using cv2.aruco.estimatePoseSingleMarkers function again. To be able to use this function we treat the way points as marker points by copying the marker size images to the initial image. These way point positions will then be used in controller to calculate the robot speed to reach the way points one by one until the main target is reached.

map() function of create_map.py file is the main module which applies these steps and	return a python list containing homogenous matrices of each target point where a	homogenous matrix of a detected pose is as follows:

Calculating Robot Pose in Way Point Coordinate Frame & Navigation of the Robot

After finding the path to follow, we take the current position of the robot coming from	real_time_image_subscriber.py and the first way point position to calculate the robot	position in the target frame. That gives us the difference in x and y axes as well as the	rotation in z axes which are the all we need to calculate the linear x and angular z speed of	the robot in order to move through the target direction.

This calculation is made by multiplication the inverse of the homogeneous robot position	matrix by the homogeneous target matrix.

Using arctan2(deltay / deltax), we calculate the orientation angle that the robot should	take, we wait until the robot fixes its angle until the error goes lower than 5 degrees, then let	it go straight forward on x axis direction.

During the orientation step, we calculate the angular z axis speed velocity of robot using w =	k_alpha * alfa equation which gives us the velocity in radians. Here, alfa is the result	comes	from alfa = np.arctan2(deltay, deltax) and k_alpha is a constant we determined as 1.	During this step, linear x velocity is 0 since we are waiting the robot to fix its orientation	before start moving towards the target.

Once the orientation angle is fixed, we calculate the linear x speed to move the robot	forward. This velocity v is calculated using v = k_p * p where p is the euclidian distance	between robot and target pose and k_p is a constant we determined as 0.8. To calculate the	euclidian distance we use deltax and deltay p = math.sqrt(deltax**2 + deltay**2). The	threshold to decide if the robot is reached the target is 0.045 meter.

In general, if the robot fixes the orientation angle, linear x speed is set to 0 and if the	robot moves straight forward, the angular z speed is set to 0. We check the orientation	error after the initial orientation, while the robot goes forward, and if the error starts to	increase again, we stop the robot’s forward speed and let it fix the orientation again. For that	step, the threshold for the orientation error is 15 degrees.

This process is running in a loop for each real time image obtained by the subscriber until	the robot reaches every way point and the target position at the end.

This task is implemented in controller.py file and here is the main parts and explanations of	this module:

pub = rospy.Publisher('/cmd_vel', Twist, queue_size=1) → main publisher to send the	calculated speed to the Turtlebot3

sub = rospy.Subscriber('/estimated_pose', MarkerPose, callback) → main subscriber to	obtain the current robot pose published from real_time_image_subscriber.py module

target_matrices = create_map.map() → Poses of the way points and final target point	calculated in the previous step are stable and they are not calculated after first initialization.	These poses are stored in this Python list variable.

callback(msg) → The callback function of subscriber. Each time a new current pose of the	robot is sent by real_time_image_subscriber, this callback function calls controller function	with the related target homogeneous matrix and robot’s.

controller(homogenous_robot,homogenous_target) → Robot’s pose in target frame is	calculated in this function. After that, according to the mode (initial orientation, going	forward or parking as we will explain in the next part), the speed is calculated as explained	above and it is published. Every time the robot reaches to a target point, this function	return True to inform callback function for sending the next target position matrix.

Since the Turtlebot3’s maximum angular velocity is 2.84 radians/sec and maximum linear	velocity is 0.22 m/sec, we determined the following constraints to be sure we don’t publish	any velocity information that may harm the robot.

if v > 0.22:
v = 0.22
elif v < -0.22:
v = -0.22

if w > 2.84:
w = 2.84
elif w < -2.84:
w = -2.84

These constraint are applied just before publishing the velocities independently from the	mode.

Parking

After reaching the final target position, the robot is parking according to the rotational	direction of the target position. We obtain this information on deltaΘ coming from the robot-	to-target homogenous matrix unlike the teta error which was coming from the arctan of	deltay and deltax during the path finding. The basic difference between these two angle	errors is that during the path finding, we rotate the robot in the target position direction by	not taking account in which direction the target positions oriented exactly. In the parking	step, we orient the robot to look exactly the same direction with the last target position. For	this purpose, we stop the robot’s linear x speed and only adjust angular z speed until the	error goes lower than 5 degrees.

parking(homogenous_robot,homogenous_target) → main function for parking step	implemented in controller.py module. This function is called after the target_reached flag is	set True at the end of the previous step.

 - A topic diagram from rviz may be added here.

Resources & Conclusion

The Construct
Emanuel Robotis
A star algosunu aldığın medium linki